## Slide 1
DEPARTMENT OF COMPUTER SCIENCE AND ENGINEERING
Project name : Smart Parking
Team name : Proj_224789_Team_3
Team members :
KANIMOZHI V(113321104036) KARAMSETTY LIKHITHA(113321104038) KARTHIKA M(113321104039)
KATHIYAYENI S(113321104041)

## Slide 2: PROJECT
A smart parking project is an innovative solution aimed at making the process of finding and managing parking spaces more efficient, convenient, and sustainable. It utilizes technology and data-driven approaches to address the challenges associated with urban and suburban parking, such as congestion, pollution, and the frustration of finding available parking spaces. Smart parking projects aim to streamline the parking process, reduce the environmental impact of urban congestion, and enhance the overall quality of life in cities and suburbs.These projects often require collaboration between government entities, private parking operators, and technology companies to be successful.

## Slide 3
Requirements:
The Components that are required are:
1.Parkng Sensors
2.Gateway/Controller
3.Cloud Platform
4.Mobile App
5.Backend Server
6.Signage And Displays
7.Cameras
8.Arduino
9.Internet Connectivity

## Slide 5: PYTHON CODE
CODE
#include <Wire.h>
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2); // Change the HEX address
#include <Servo.h>
Servo myservo1;
int IR1 = 2;
int IR2 = 4;
int SmokeDetectorPin = 6; // Digital pin for the smoke detector
int BuzzerPin = 7; // Digital pin for the buzzer
int Slot = 4; // Enter Total number of parking Slots
bool flag1 = false;
bool flag2 = false;
unsigned long lastLcdUpdate = 0; // Variable to track the time of the last LCD update
unsigned long lcdUpdateInterval = 1000; // Update the LCD every 1000

## Slide 6
void setup() {
lcd.begin(16, 2); // Initialize LCD with 16 columns and 2 rows
lcd.backlight();
pinMode(IR1, INPUT);
pinMode(IR2, INPUT);
pinMode(SmokeDetectorPin, INPUT);
pinMode(BuzzerPin, OUTPUT);
myservo1.attach(3);
myservo1.write(100);
lcd.setCursor(0, 0);
lcd.print(" ARDUINO ");
lcd.setCursor(0, 1);
lcd.print(" PARKING SYSTEM ");
delay(2000);
lcd.clear();
Serial.begin(9600); // Start serial communication for debugging
}

## Slide 7
if (digitalRead(IR2) == LOW && !flag2) {
flag2 = true;
if (!flag1) {
myservo1.write(0);
Slot++;
}
}
if (flag1 && flag2) {
delay(1000);
myservo1.write(100);
Serial.println("Servo returned to initial position.");
flag1 = false;
flag2 = false;
}
// Update the LCD display with a delay
if (millis() - lastLcdUpdate >= lcdUpdateInterval) {
updateLcdDisplay();
lastLcdUpdate = millis();
}

## Slide 8
void updateLcdDisplay() {
if (digitalRead(SmokeDetectorPin) == HIGH) {
displayMessage(" WARNING! ", " Smoke Detected ");
digitalWrite(BuzzerPin, HIGH); // Turn on the buzzer
} else {
displayMessage(" WELCOME! ", "Slot Left: " + String(Slot));
digitalWrite(BuzzerPin, LOW); // Turn off the buzzer
}
}
void displayMessage(const char *line1, const String &line2) {
lcd.clear();
lcd.setCursor(0, 0);
lcd.print(line1);
lcd.setCursor(0, 1);
lcd.print(line2);
}

## Slide 9: CONCLUSION:
The smart parking project has demonstrated the potential to revolutionize urban mobility and enhance the overall parking experience for both drivers and city authorities. Through the deployment of advanced technologies, data analytics, and improved infrastructure, this project aims to address various challenges associated with parking in urban areas.The success of this project underscores the potential for further innovation in the realm of smart cities and transportation. As technology continues to evolve, smart parking solutions will play an increasingly vital role in creating more sustainable, efficient, and user-friendly urban environments.

## Slide 10
THANK YOU